## Slide 1
+
−
Operational Amplifiers
Principles of Op-Amps
Presented by: Nandini Mavillapalle
1st Semester M.Sc. EE Student
16.07.2026
Notes: Introduce the topic: operational amplifiers and their principles — the active building block behind the read-out electronics of the cantilever/PSD experiment.

## Slide 2
What is an operational amplifier?
V₊
V₋
Vₒᵤₜ
+Vs
−Vs
Figure 1: Op-amp circuit symbol
A high-gain, DC-coupled voltage amplifier with two inputs and one output.
It amplifies only the difference between the non-inverting input (V₊) and the inverting input (V₋).
Powered by a dual supply (+Vs, −Vs); the output swings between these rails.
The fundamental building block of analog signal processing — amplifying, filtering, and mathematical operations on signals.
Ideal transfer: Vₒᵤₜ = A (V₊ − V₋), with open-loop gain A → very large.
Topic 4
16.07.2026 | 2
Notes: An op-amp is a high-gain voltage amplifier with two inputs and one output, run from a dual supply. It amplifies only the difference between the two inputs by a very large factor A. It is the fundamental building block of analog electronics.

## Slide 3
Principles of Op-Amps
1
Differential amplification Responds only to the difference of its inputs: Vₒᵤₜ = A (V₊ − V₋).
2
Very high open-loop gain (A) Raw gain is enormous (~10⁵–10⁶); feedback tames it into a precise value.
3
Very high input impedance The inputs draw almost no current, so the op-amp does not load the source.
4
Very low output impedance The output can drive a load without its voltage dropping.
5
Works with negative feedback Gives the two golden rules: V₊ = V₋ (virtual short) and no input current.
6
High common-mode rejection Rejects signals common to both inputs (noise, drift); amplifies only the difference.
Topic 4
16.07.2026 | 3
Notes: The six principles the topic rests on: differential amplification, very high gain, high input impedance, low output impedance, negative-feedback operation (golden rules), and high common-mode rejection.

## Slide 4
The ideal op-amp & the two golden rules
V₊
V₋
Vₒᵤₜ = Aₒₗ (V₊ − V₋)
Ideally it amplifies the difference of its inputs with infinite open-loop gain.
Ideal parameters
Open-loop gain Aₒₗ
→ ∞
Input impedance Zᵢₙ
→ ∞
Output impedance Zₒᵤₜ
→ 0
Bandwidth
→ ∞
CMRR(Common Mode Rejection Rate)
→ ∞
The two golden rules
(hold with negative feedback)
1
Virtual short
Feedback drives Vₒᵤₜ until V₊ = V₋ — no voltage difference across the inputs.
2
No input current
Infinite Zᵢₙ means the inputs draw no current — it all flows through the feedback network.
Topic 4
16.07.2026 | 4
Notes: The ideal op-amp: infinite gain, infinite input impedance, zero output impedance. With negative feedback these give the two golden rules — inputs at the same voltage (virtual short), and no input current — which let us solve any op-amp circuit by inspection.

## Slide 5
The two golden rules — in depth
Precondition: the rules hold only with negative feedback — part of the output must return to the inverting (−) input.
Rule 1 — Virtual short: V₊ = V₋
Vₒᵤₜ = A (V₊ − V₋) with A ~ 10⁵–10⁶.
Vₒᵤₜ is finite (limited by the rails), so the input difference V₊ − V₋ is only a few µV ≈ 0.
Feedback self-corrects: if V₋ dips, Vₒᵤₜ rises and pushes V₋ back up until balance.
If the (+) input is grounded, the (−) input becomes a virtual ground (0 V).
Rule 2 — No input current
Input impedance is (near) infinite; only a tiny bias current, pA–nA, flows.
That current is negligible next to the resistor currents → treat it as zero.
So all signal current flows through the external feedback network, never into the op-amp.
This lets you write a clean KCL node equation at the (−) input.
Caveats: the residual input difference grows with frequency; offset voltage & bias current matter for tiny signals; the rules fail if the output saturates or if there is no negative feedback.
Topic 4
16.07.2026 | 5
Notes: In depth: the two golden rules hold only under negative feedback. Rule 1 — because the open-loop gain A is enormous and the output is finite, the input voltage difference Vout/A is only microvolts, so the two inputs are effectively at the same voltage; the feedback loop actively maintains this, and with the plus input grounded the minus input is a virtual ground. Rule 2 — the input impedance is essentially infinite, so the inputs draw negligible current and all current flows through the feedback network, which lets us apply KCL at the inverting node. Caveats: the virtual short is only approximate (Vout/A, worse at high frequency), offset and bias errors matter for small signals, and the rules break if the output saturates or feedback is absent.

## Slide 6
Worked theory 1 — the inverting amplifier
−
+
Rin
Vᵢₙ
Rf
Vₒᵤₜ
virtual ground
Figure 2: Inverting amplifier
Step-by-step (using the golden rules)
1
Virtual short
The (+) input is grounded, so feedback holds the (−) input at 0 V — a virtual ground.
2
No input current
No current enters the op-amp, so the input current continues through Rf.
3
KCL at the (−) node
Vᵢₙ
Rin
=
−
Vₒᵤₜ
Rf
Result:
Vₒᵤₜ = −
Rf
Rin
· Vᵢₙ
Topic 4
16.07.2026 | 6
Notes: Derivation of the inverting amplifier. The non-inverting input is grounded; by the virtual-short rule the inverting input sits at a virtual ground of 0 V. By the no-input-current rule, the input current Vin/Rin flows entirely through Rf. Kirchhoff's current law at the node gives Vin/Rin = −Vout/Rf, so Vout = −(Rf/Rin)·Vin. The gain is set only by the resistor ratio.

## Slide 7
Worked theory 2 — the non-inverting amplifier
+
−
Vᵢₙ
R1
Rf
Vₒᵤₜ
Figure 3: Non-inverting amplifier
Step-by-step (using the golden rules)
1
Virtual short
V₋ = V₊ = Vᵢₙ, so the R₁–Rf divider sees Vₒᵤₜ across it and Vᵢₙ at its tap.
2
Current in R₁
3
Same I through Rf
No input current, so that same I flows through Rf: Vₒᵤₜ = Vᵢₙ + I·Rf.
I =
Vᵢₙ
R₁
(from the − node to ground)
Result:
Vₒᵤₜ = ( 1 +
Rf
R₁
) · Vᵢₙ
Topic 4
16.07.2026 | 7
Notes: Derivation of the non-inverting amplifier. By the virtual-short rule, the inverting input equals the signal at the non-inverting input, Vin. The resistors R1 and Rf form a divider from the output to ground with its tap at the inverting node held at Vin. The current through R1 is Vin/R1, and since no current enters the op-amp the same current flows through Rf, giving Vout = Vin + (Vin/R1)Rf = Vin(1 + Rf/R1). The gain is always at least one, and the input impedance is very high.

## Slide 8
The real op-amp: non-idealities that matter
Finite gain, finite bandwidth and small DC errors set the true limits of a precision circuit.
Aₒₗ
10⁵–10⁶
Finite open-loop gain — large but not infinite; sets closed-loop accuracy.
GBW
~1–100 MHz
Gain–bandwidth product: gain × bandwidth is constant.
SR
V/µs
Slew rate limits how fast Vₒᵤₜ can change for large signals.
Vₒₛ
µV–mV
Input offset voltage — a DC error added at the input.
Iᵦ
pA–nA
Input bias current — critical when sensing tiny currents.
CMRR
80–120 dB
Common-mode rejection: how well it ignores shared signals.
Topic 4
16.07.2026 | 8
Notes: Real devices depart from the ideal. Finite gain and the gain-bandwidth product cap accuracy and speed; slew rate limits large fast signals; offset voltage and bias current add DC errors; finite CMRR limits rejection of common-mode signals. For precision measurements these are the effects to respect.

## Slide 9
Frequency response & bandwidth
Gain (dB)
Aₒₗ
−20 dB / decade
0 dB
fT
Frequency (log scale) →
Figure 4: Open-loop gain vs frequency (Bode plot) [3]
1
Open-loop gain is huge at DC but falls as frequency rises (~ −20 dB per decade).
2
Gain × bandwidth = constant = the unity-gain frequency fT.
3
More closed-loop gain therefore means less bandwidth — a direct trade-off.
4
Above fT the gain drops below 1 and the op-amp can no longer amplify.
Topic 4
16.07.2026 | 9
Notes: The op-amp's enormous gain is only available at low frequencies; open-loop gain rolls off at about −20 dB/decade. The gain-bandwidth product is constant, equal to the unity-gain frequency f_T. Higher closed-loop gain means proportionally less bandwidth. Above f_T the op-amp can no longer amplify.

## Slide 10
Conclusion
1
A differential amplifier
The op-amp amplifies only V₊ − V₋, with a very high open-loop gain.
2
Two golden rules
Under negative feedback: virtual short (V₊ = V₋) and no input current.
3
Gain set by feedback
Inverting and non-inverting gains are both fixed by the external resistor ratio — set by the resistors, not by the op-amp.
4
Respect the real limits
Offset, bias current, finite gain-bandwidth, slew rate and CMRR bound real performance.
Topic 4
16.07.2026 | 10
Notes: Summary of topic 4: the op-amp is a high-gain differential amplifier; under feedback it obeys the two golden rules; the closed-loop gain is set by external resistors; and real devices have limits we must respect. These principles underpin every op-amp circuit, including the PSD read-out covered in the next topic.

## Slide 11
References
[1] Texas Instruments, “Handbook of Operational Amplifier Applications,” Application Report SBOA092B, 2016.
[2] P. Horowitz and W. Hill, The Art of Electronics, 3rd ed. Cambridge University Press, 2015.
[3] S. Franco, Design with Operational Amplifiers and Analog Integrated Circuits, 4th ed. McGraw-Hill, 2015.
[4] A. S. Sedra and K. C. Smith, Microelectronic Circuits, 7th ed. Oxford University Press, 2015.
[5] R. Mancini (ed.), Op Amps for Everyone, Texas Instruments, 2002.
Topic 4
16.07.2026 | 11
Notes: Standard references for operational-amplifier theory used in preparing this talk.

## Slide 12
Vielen Dank!
Presented by: Nandini Mavillapalle
1st Semester M.Sc. EE Student
Notes: Thank you — happy to take questions on the principles of operational amplifiers.